## Slide 1: National efforts to address space weather risks and customer needs
Mamoru Ishii
Space Weather and Environment Informatics Laboratory
Applied Electromagnetic Research Institute
National Institute of Information and Communications Technology
4-2-1 Nukui-kita, Koganei 184-8795 JAPAN
Notes: Good morning. I am Mamoru Ishii from National Institute of Information and communications technology. Today I would like to introduce our activity of space weather.

## Slide 2: NICT Space Weather Forecast Center
Real-time space weather monitoring
Simulation results
Flare forecast
Magnetic field forecast
High-energy particle forecast
HF propagation forecast
Web access:
158,057/month
（May, 2013）
No. of e-mail addressee：
9,271
Forecast information and data exchange and sharing among ISES SW forecast center
Domestic users: satellite operator, aviation office and companies, power plant companies, HF telecommunicator /broadcaster, resource survey, Univ. and research institutes, amateur HF operators
Solar activity and space environment are provided with Web, email RSS and FAX. Press release for significant event.
Notes: We manage operational space weather forecast. We have a briefing of space weather at 2;30pm every day and provide forecast information on 3pm via email, web and FAX. The forecast items are flare, magnetic field, high-energy particle and HF propagation. Web access is about 160 thousand every month and the number of email adressee is over nine thousand. The main users of our information are satellite operator, aviation office and companies, power plant companies and so on.

## Slide 3: Communications with customers
・Survey of potential space weather customers
Period：2013-14
method：
Mapping of potential customers
Extract the address of potential customers
Contact by telephone (23 fields 50 organizations)
face to face interview (10 organizations)
Airplane pilot, resource survey, power plant,
aviation, management of astronouts ,
Needs: provide SWx information even if the user has no knowledge of SWx, training program of SWx
Action: renewal of Web, building training program of SWx
・SWx users forum
General information of SWx
How to use NICT SWx data
Guest speakers relative to SWx

## Slide 4: Mapping of potential customers

## Slide 5: Relation of Needs-Seeds in SWx
Disturbance of magnetosphere
Disturbance of ionosphere
Satellite anomary
Hazard to telecom, broadcast
Hazard to aviation
Hazard to power line
Hazard to human activity in space
Hazard to positioning
Human radiation
HF propagation
GIC
Disability of GNSS
Hazard to satellite operation
Ground conductivity distribution
Soalr flare
CME/CIR
Coronal Hall
High speed
solar wind
Plasma cloud
X-ray
Increase of high energy particle
Increase radiatoin
Ionization of lower ionophsere
Increase of high energy particle
Increase of ionospheric current
Increase of electron density
Expanding upper atmosphere
Change the satellite orbit
Sun
IPS
Magnetosphere/Ionosphere
influence
Social hazard/needs
Solar Terr. Phys.
SWx the social needs
Death Valley
Death Valley
Study of nknown process
SWx becomes Indispensable information for their task
Academic institute
society

## Slide 6
Magnetometer
Ionosonde
Sun and Solar wind
HF radar
Syowa, Antarctica
NICT SWx Obs. Network
Far East Mag.＆HF radar network
Operational Ionosphere Obs. Network ＆Sun and Solar obs. systems
SEALION
ACE receiver antenna
Mar. 2014
Solar Radio telescope
Mar. 2014
New Ionosonde
system
Oct. 2014
Mar. 2015
2016-2020?

## Slide 7: Available Data
Observing data
  Domestic and antarctic ionogram since IGY
  SEALION ionogram, GPS and scintillation data
  Magnetometer data
  Solar radio data : Hiraiso(present) and Yamagawa(near future)
Simulation data archive
  Comparing with observation results for evaluation and scientific discussion
  MHD magnetosphere model
  GAIA: atmospheric/ionospheric model

## Slide 8: Model/simulation
Ion density (alt.300km）
Surface temperature
Snap shot example of Atmosphere-Ionosphere connection model “GAIA” with meteorological realistic analysis data
Even in dynamic pressure (V*V*D) is
same, magnetospheric impact is more severely affected by velocity increase
-40
40
0
J0 E0 =4.0×10-13[W/m3]
Increase dynamo current
Empirical Model
Numerical code
Ionosphere
Radiation belt
Density increase
Velocity increase
TEC map forecast system using season and solar activity as input parameters
Empirical model of radiation belt using multi-parameter as input parameters
Notes: This is schematic plot shown our model and simulation activity. Vertical and horizontal axis shows the kinds of model and their region, respectively.
This is TEC map forecasting model with empirical code, this is the model named GAIA which is connecting numerical code from the ground to the ionosphere. This is the initial results of long-term variation of NmF2. The result still has some difference between observatoin and the simulation and now we are improving the code.
This is the empirical model of radiation belt using multi-parameter as input parameters which is already on service, and this is the magnetospheric numerical code . This case shows that even in the same dynamic pressure, magnetosphere is more sensitive to velocity variation.

## Slide 9: Highest priority needs – Ionospheric information above ocean
Precise ionospheric model is necessary for use of aviation and radio infrastructure, e.g., telecommunication, broadcast and GNSS.
For that, It is necessary to get ionospheric information above ocean.
Candidate of observation methods
  Oblique sounding with ionosonde
  Trans equatorial propagation
  GPS buoy
  Satellite occultation

## Slide 10: Trans-Equatorial Propagation (TEP)
Oarai
Melbourne
Radio Austlaria
Equatorial Ionospheric
disturbances

## Slide 11: Oblique sounding with ionosondes
NICT are now routinely operates oblique sounding ionogram every 15 min.
NICT and KSWC are discussing international oblique sounding project with VIPIR system.
Development and observation with simple receivers will make possible to increase observation points.

## Slide 12: agenda
Customers and national needs (or potential customers if you are considering new services)
Services you provide (or that you are considering providing)
Data you use and make available (or that you need)
Highest priority needs
How others can benefit from your data, services, customer knowledge, etc.

## Slide 13: Unify/simplify of Web structure
Unify the forecast/data site which are operating independently
Unify the Web server into NICT information system office
Necessity to provide huge No. of SWx data with high security
Increase of data needs and new observation, solar radio, VIPIR
Complicated structure with long-period operation
Background
Unifying Web server on NICT information system office
Provide new observation data
Easy access of data by restructuring the Web
Actions
Observation/simulation in domestic/international
present：several independent system